## Slide 1: CERTA Certification Course

## Slide 2: Course flow
Introduction
General Requirements
Pre-job Planning and Preparation
Propane Tool and Equipment Safety
Application Safety
Post-job Requirements and Duties
Hands-on Torching
Exam

## Slide 3: Certa safety practices
Checklist
Pre-job Planning
Application
Torching Safety
Fire Watch Requirements

## Slide 4: General requirements
Section 1

## Slide 5: During this section you should be able to:
1. List personal protective equipment requirements for torching activities
2. Describe basic first-aid procedures associated with torching activities
3. Describe the PASS system for using a fire extinguisher

## Slide 6: pull
Pull out the ring pin while holding the fire extinguisher upright. This will snap the safety seal.

## Slide 7: aim
Aim the hose at the base of the fire. Start upwind and approach the fire cautiously.

## Slide 8: Squeeze and sweep
Squeeze the lever to discharge the extinguisher.
Sweep the spray from side to side.

## Slide 9: Class a
Wood
Paper
Plastic
Rags

## Slide 10: Class b
Gas
Oil
Grease
Paint

## Slide 11: Class C
Electric

## Slide 12: Class D
Metal

## Slide 13
A minimum of ____
4A60BC fire
extinguishers should be
readily available
within 10 feet of all
torching activities.
What does the plastic
seal band through the
release pin of a fire
extinguisher ensure?
Name one thing you
should do
and
one thing you
should not do
when tending to a
burn victim.
Name two things that
should be done for
victims of propane
freeze burn.
What words does the term
PASS stand for?
Name two materials that—
if they were on fire—
would be classified as
Class A fires.
Name three types of PPE
that should be used while
doing torch work.
What classification of
fire extinguisher should
be within 10 feet of
torch work?
What should be done with
a fire extinguisher that
has been discharged?

## Slide 14: Can you:
1. List personal protective equipment requirements for torching activities?
2. Describe basic first-aid procedures associated with torching activities?
3. Describe the PASS system for using a fire extinguisher?

## Slide 15: Pre-job Planning and Preparation
Section 2

## Slide 16: During this section you should be able to:
1. Identify the key elements of a comprehensive pre-job inspection
2. Prescribe hazard controls when torching near hazardous areas

## Slide 18: Can you:
1. Identify the key elements of a comprehensive pre-job inspection?
2. Prescribe hazard controls when torching near hazardous areas?

## Slide 19: Propane Tool and Equipment Safety
Section 3

## Slide 20: During this section you should be able to:
1. Name the components of a roofing torch assembly
2. Explain the proper steps and procedures for handling propane gas cylinders

## Slide 21: Propane tank

## Slide 22: Propane tank
With regulator

## Slide 23: Liquid & vapor withdrawal

## Slide 25: Can you:
1. Name the components of a roofing torch assembly?
2. Explain the proper steps and procedures for handling propane gas cylinders?

## Slide 26: application safety
Section 4

## Slide 27: During this section you should be able to:
1. Recognize hazardous areas
2. Describe safe torching techniques to use near hazardous areas

## Slide 29
Hazard 1

## Slide 30
Hazard 2

## Slide 31
Hazard 3

## Slide 32
Hazard 4

## Slide 33
Hazard 5

## Slide 34
Hazard 6

## Slide 35
Hazard 7

## Slide 36
Hazard 8

## Slide 37
Hazard 9

## Slide 38
Hazard 10

## Slide 39
Hazard 11

## Slide 40
Hazard 12

## Slide 42: Can you:
1. Recognize hazardous areas?
2. Describe safe torching techniques to use near hazardous areas?

## Slide 43: Fire watch requirements and duties
Section 5

## Slide 44: During this section you should be able to:
1. Explain the post-job fire watch and other duties

## Slide 47: Can you:
1. Explain the post-job fire watch and other duties?

## Slide 48: Hands-on torching

## Slide 49: During this section you should be able to demonstrate:
1. Proper torch-lighting procedures.
2. Proper torch shut-down procedures.
3. Application of self-adhering base ply with a focus on ensuring sealed laps, using a flashing box mock-up.
4. Flashing torch-and-flop application using a flashing box mock-up.
5. Flashing direct torching application using a flashing box mock-up and a detail application-size (105k Btu or less) torch.
6. Proper starting of field membrane rolls at roof edges or walls.
7. Torch-and-flop method for going around a pipe penetration and a drain.
8. Torch-and-flop method for installing field sheet over a drain penetration.
9. Torch-and-flop method for ending field membranes at roof edges or walls.
10. Ability to evaluate and rate others’ torching behaviors.

## Slide 50: exam

## Slide 51: CERTA Certification Course